| Testing Conducted By: BUTE-TMIT Telecommunications Test Laboratory |
| --- |
| ID | 297 | Job No | 1000027 |
| Customer | xxxxxxx |
| Product | xxxxxxxxxxxxxxxxxxxxxxxxxxxxxx |
| Specification | ETSI TS 101 388 |
| Clause | 5.5.3(c) |
| Purpose Of Test | To confirm the loop reach of the EUT operating FDD ADSL Over ISDN at 1024kbps downstream |
| EUT Details | Sample Number: 0001, Modification State: 00 |
| Operating State |  |
| Test Class | Formal Test | Engineer | kovacs |
| Date & Time | Fri 24/Mar/2006 14:22:47 | Temp | 26.95°C | Humidity | 11.78% |
|  |  | Tested With Auto Test Run (EUT Master): Yes |
| Test Result |
| Overall Test Status: Pass |
| Detailed Results |
| Modem Settings Traffic Direction: Downstream Technology: FDD ADSL over ISDN Path: Interleaved Trellis Coding: On Noise Margin: 6dB Test Condition Payload Bitrate (kbps) Test Loop Loop Length Noise Model Noise Level TX Frames RX Frames BERT Status 1 1024 0 0dB FA 6dB 83340 83340 0.00E+00 Pass 2 1024 1 37dB FA 6dB 83340 83340 0.00E+00 Pass 3 1024 2 34.5dB FA 6dB 83340 83340 0.00E+00 Pass 4 1024 3 35.5dB FA 6dB 83340 83340 0.00E+00 Pass 5 1024 4 35dB FA 6dB 83340 83340 0.00E+00 Pass 6 1024 5 35dB FA 6dB 83340 83340 0.00E+00 Pass 7 1024 6 35dB FA 6dB 83340 83340 0.00E+00 Pass 8 1024 7 33.5dB FA 6dB 83340 83340 0.00E+00 Pass 9 1024 8 40.5dB FA 6dB 83340 83340 0.00E+00 Pass |

| Testing Conducted By: BUTE-TMIT Telecommunications Test Laboratory |
| --- |
| ID | 308 | Job No | 1000027 |
| Customer | xxxxxxxxxxxxxxx |
| Product | xxxxxxxxxxxxxxxxxxxxx |
| Specification | ETSI TS 101 388 |
| Clause | 5.5.3(v) |
| Purpose Of Test | To confirm the loop reach of the EUT operating FDD ADSL Over ISDN at 6144kbps downstream |
| EUT Details | Sample Number: 0001, Modification State: 00 |
| Operating State |  |
| Test Class | Engineering Test | Engineer | kovacs |
| Date & Time | Wed 29/Mar/2006 15:33:00 | Temp | 23.65°C | Humidity | 29.95% |
|  |  | Tested With Auto Test Run (EUT Master): No |
| Test Result |
| Overall Test Status: Fail |
| Detailed Results |
| Modem Settings Traffic Direction: Downstream Technology: FDD ADSL over ISDN Path: Interleaved Trellis Coding: On Noise Margin: 6dB Test Condition Payload Bitrate (kbps) Test Loop Loop Length Noise Model Noise Level TX Frames RX Frames BERT Status 1 6144 0 0dB FB 6dB 83340 83340 0.00E+00 Pass 2 6144 1 13dB FB 6dB 83340 83340 0.00E+00 Pass 3 6144 2 10dB FB 6dB 83340 0 1.00E+00 Fail |